## Slide 1: Energy scale cross-calibration of Hyper-Kamiokande detector using Deuterium-Tritium neutron generator
Abderrazaq El Abassi; Rafik Er-rabit, Mohamed Gouighri
References
[1] Super-K collaboration: 16N as a calibration source for Super-Kamiokande : https://doi.org/10.1016/S0168-9002(00)00900-1
[2] M.Pillon: Measurement of the 16,17O(n,p)16,17N cross sections for validating the water activation experiment for ITER at the Frascati neutron generator: https://doi.org/10.1016/j.nima.2021.165107
[3] J.k.Bienlein: the half life of 16N: https://doi.org/10.1016/0029-5582(64)90202-0
[4] HK software: Water Cherenkov Simulation built on top of Geant4; BONSAI and FLOWER are reconstruction algorithms : https://github.com/WCSim/WCSim
higgstan.com: https://higgstan.com
Hyper-Kamiokande detector
is a next-generation long
baseline neutrinos experiment
expected to start taking data in 2027
Neutron activation simulation[1]
Preliminary results: 16N MC truth position
Preliminary results: 16N properties
Conclusions
Preliminary results indicates that the water activation simulation
and 16N decay have been achieved, In particular, our 16N yield appears to be higher when compared to previous
Super-K[1] result.
The reconstructed energy is dominated by 6.1 MeV gammas in coincidence with 4.3 MeV electron endpoint energy
Next step is to reproduce the SK[1] results, adapt the simulation to HK environment, and identify a calibration strategy for deployment locations.
Preliminary results: Reconstructed vertex and energy
The DTG generates neutrons by colliding deuterium and tritium ions with a fixed metal hydride target, containing equal parts of deuterium and tritium.
The neutron generator can be pulsed at maximum rate of 100 Hz, with each pulse yielding approximately 106 neutrons.
16N properties and beta spectrum
Capture cross section on 16O on agreement with ITER measaurement[2]
The mean distance traveled by neutrons before 16N creation is 15.47 cm
Mean time before 16N creation is 3.08 ns
16N samples are used as input
for WCSim[4] toolkit
The decay product is propagated throughout the detector Volume
• The peak of energy is around 6 MeV which corresponds to the dominant gamma ray.
• Above a certain threshold (between 5 and 6 MeV), the shape of the energy spectrum can be fit with a Gaussian.
• At lower energies, the distribution appears to be affected by a cut in the shape due to detector's efficiency.
2H + 3H → 4He + n
16N beta decays plus a gamma particle coming from 16O dexcitation
16N -> 16O + e- + ⊽e + ɣ
Hyper-K
expected 16N yield is 2.3%, while
Super-K[1] results found 1.3% and 1% observed in their data.
27.7% of 16N will decay directly to the ground state of 16O. The 6.129 MeV gamma ray is dominant with a fraction of 67.2%.
Deuterium-Tritium neutron generator is used to cross check the energy scale
DTG overcome some limitations of LINAC, such as isotropy and lower dead time, and lower shadowing effect.
16N is created by a neutron capture on 16O, and used as a source of calibration[1] to be compared with LINAC calibration and combine both results to evaluate the total absolute energy scale.
Deuterium-Tritium neutron generator
16N yield[%] and total cross section
Visualization of generated neutron tracks in water
BONSAI[4] recconstruted vertex, and FLOWER[4] reconstructed energy
WCSim[4] :16N x and y, z positions, the neutrons were directed towards –z
Reconstructed mean values are close to truth mean values, 0.02 cm, 0 cm, and –13.73 cm for truth mean vtx_x, vtx_y, and vtx_z respectively. However, a wider distribution spread due to the resolution of the detector is observed, where is around 14
DTG deployment
Electron energy is less than 4.3 MeV
DTG is a low energy cross calibration system.
Used to generate an N16 cloud inside the inner detector:
  168O + 10n → 10n + 167N
This N16 cloud beta decays isotopically:
  16N → 16O* + ν̅ + e
DTG device will be deployed through several calibration ports into different depths per port.
After firing the neutrons, the device will be raised above the source before data taking to minimize shadowing effect.
Consistent with Super-K[1] results
GEANT4 simulation of a 4x4x4 m3 box of water
• Number of simulated
neutrons: 5M
• Neutrons energy: 14.2 MeV
• Orientation: at the origin (0,0,0) directed towards -Z axis with an opening angle of 15 degrees.